## Slide 1
存储器层次结构（1）
王晶
jwang@ruc.edu.cn，信息楼124
2023年12月

## Slide 2: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 3: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 4
A Computing System
Three key components
Computation
Communication
Storage/memory
Burks, Goldstein, von Neumann, “Preliminary discussion of the
logical design of an electronic computing instrument,” 1946.
Image source: https://lbsitbytes2010.wordpress.com/2013/03/29/john-von-neumann-roll-no-15/

## Slide 5: 你认识它们吗？
（2）
（1）
（3）
（5）
（4）
（6）

## Slide 7: Random-Access Memory (RAM)
Key features
  Basic storage unit is normally a cell (one bit per cell).
  RAM is traditionally packaged as a chip.
  Multiple RAM chips form a memory.
RAM comes in two varieties:
  SRAM (Static RAM)
  DRAM (Dynamic RAM)

## Slide 8
静态 RAM 基本电路的 读 操作
A´
T1 ~ T4
T5
T6
T7
T8
A
写放大器
写放大器
DIN
写选择
读选择
读放
位线A
位线A
´
列地址选择
行地址选择
DOUT
行选
T5、T6 开
T7、T8 开
列选
读放
DOUT
VA
T6
T8
DOUT

## Slide 9
动态RAM（DRAM）存储元电路
读出时数据线有电流 为 “1”
数据线
C
s
T
字线
0
1
写入时 CS 充电 为 “1” 放电 为 “0”
T
无电流
有电流

## Slide 10: RAM Technologies
DRAM
1 Transistor + 1 capacitor / bit
  Capacitor oriented vertically
Must refresh state periodically
SRAM
6 transistors / bit
Holds state indefinitely
静态RAM(SRAM)：更快，更贵，主要用作高速缓存存储器，可以在CPU芯片上，也可以在片下，容量从几MB到几十MB
动态RAM(DRAM)：用作主存及外部存储设备缓存，相对SRAM较慢，价值相对更低，容量达到GB甚至TB级
SRAM与DRAM共同的缺点：易失性存储，断电后数据丢失

## Slide 11: SRAM vs DRAM Summary
Trends
  SRAM scales with semiconductor technology
    Reaching its limits
  DRAM scaling limited by need for minimum capacitance
    Aspect ratio limits how deep can make capacitor
    Also reaching its limits
Trans. Access Needs Needs
per bit time refresh? EDC? Cost Applications
SRAM 6 or 8 1x No Maybe 100x Cache memories
DRAM 1 10x Yes Yes 1x Main memories,
frame buffers
EDC: Error detection and correction

## Slide 12: 总线结构互联的CPU和存储器
总线(bus)：在处理器和DRAM主存之间传输数据流的共享电子电路
总线事务(bus transaction)：CPU和主存之间传送数据的一系列步骤
  读事务(read transaction)：从主存传送数据到CPU
  写事务(write transaction)：从CPU传送数据到主存
总线是一组并行的导线，能够携带地址、数据和控制信号；两个以上的设备也能共享同一总线
Main
Memory
主存
I/O bridge
I/O桥
Bus interface
总线接口
ALU
Register file
寄存器文件
CPU芯片
System bus
系统总线
Memory bus
内存总线

## Slide 13: 内存器读操作
Movq A, %rax
读事务的三个操作步骤：
  CPU将地址A放到系统总线上
ALU
Register file
Bus interface
A
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 14: 内存器读操作
Movq A, %rax
读事务的三个操作步骤：
  CPU将地址A放到系统总线上
  主存从内存总线读地址A，从DRAM取出数据，并写到内存总线
ALU
Register file
Bus interface
x
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 15: 内存器读操作
Movq A, %rax
读事务的三个操作步骤：
  CPU将地址A放到系统总线上
  主存从内存总线读地址，从DRAM取出数据，并写到内存总线
  CPU从系统总线上读数据，并复制到寄存器%rax中
ALU
Register file
Bus interface
x
0
A
x
Main memory
I/O bridge
%rax
Load operation: movq A, %rax

## Slide 16: 内存器写操作
Movq %rax, A
写事务的三个操作步骤：
  CPU将地址A放到系统总线上
y
ALU
Register file
Bus interface
A
0
A
Main memory
I/O bridge
%rax
Store operation: movq %rax, A

## Slide 17: 内存器写操作
Movq %rax, A
写事务的三个操作步骤：
  CPU将地址A放到系统总线上
  CPU将%rax中的数据复制到系统总线
y
ALU
Register file
Bus interface
y
0
A
Main memory
I/O bridge
%rax
Store operation: movq %rax, A

## Slide 18: 内存器写操作
Movq %rax, A
写事务的三个操作步骤：
  CPU将地址A放到系统总线上
  CPU将%rax中的数据复制到系统总线
  主存从内存总线读出数据，并将这些位存储到DRAM中
y
ALU
Register file
Bus interface
y
0
A
Main memory
I/O bridge
%rax
Store operation: movq %rax, A

## Slide 19: 传统的DRAM
128位16×8的DRAM芯片视图
  芯片由r行×c列=d个超单元（suppercell）组成
  超单元由w位组成，芯片共有d×w位存储信息
  示例：4行、4列、8位存储单元总存储容量为： 4×4×8=128位
1(01)
0(00)
3(11)
2(10)
列地址(CAS)
行地址
(RAS)
DRAM芯片
内部行缓冲区
内存 控制器
CPU
地址引脚
2位
数据引脚
8位
0(00)
1(01)
2(10)
3(11)
8位

## Slide 20: 传统的DRAM
128位16×8的DRAM芯片视图
  芯片由r行×c列=d个超单元（suppercell）组成
  超单元由w位组成，芯片共有d×w位存储信息
  示例：4行、4列、8位存储单元总存储容量为： 4×4×8=128位
1(01)
0(00)
3(11)
2(10)
列地址(CAS)
行地址
(RAS)
DRAM芯片
内部行缓冲区
内存 控制器
CPU
地址引脚
2位
数据引脚
8位
0(00)
1(01)
2(10)
3(11)
8位
读取超单元(2,1)
RAS=2

## Slide 21: 传统的DRAM
128位16×8的DRAM芯片视图
  芯片由r行×c列=d个超单元（suppercell）组成
  超单元由w位组成，芯片共有d×w位存储信息
  示例：4行、4列、8位存储单元总存储容量为： 4×4×8=128位
1(01)
0(00)
3(11)
2(10)
列地址(CAS)
行地址
(RAS)
DRAM芯片
内部行缓冲区
内存 控制器
CPU
地址引脚
2位
数据引脚
8位
0(00)
1(01)
2(10)
3(11)
8位
读取超单元(2,1)
CAS=1
内存访问特点：
先行后列
行先缓存于row buffer
从row buffer中访问列
二维阵列组织优缺点：
优点：引脚数量少
缺点：两步发送地址，增加访问时间

## Slide 22: 4. 内存模块
DIMM：双列直插内存模块(Dual Inline Memory Module, DIMM)
以64位为块传送数据到内存控制器和从内存控制器传出数据
访问地址A处机器字：
  内存控制器将地址A转换为超单元地址(i,j)，发送到内存模块，
  内存模块将(i,j)广播到每个DRAM模块，每个DRAM模块输出(i,j)超单元内容
  模块中电路收集这些输出，合并成一个64位字，返回给内存控制器
: supercell (i,j)
64 MB内存模块
由8个8Mx8 DRAM组成
addr (row = i, col = j)
内存控制器
DRAM 7
DRAM 0
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56
位于主存地址A处的64位机器字
bits
0-7
bits
8-15
bits
16-23
bits
24-31
bits
32-39
bits
40-47
bits
48-55
bits
56-63
64位机器字
0
31
7
8
15
16
23
24
32
63
39
40
47
48
55
56

## Slide 23
1. 容量为1024B的存储空间，地址线需要 [填空1] 位
2. 某计算机字长16位，主存地址空间大小64KB，按字节编址，寻址范围 [填空2] 到 [填空3]
作答
填空题
3分

## Slide 24: 练习题
r表示一个DRAM阵列中的行数，c表示列数，br表示行寻址需要的位数，bc表示列寻址需要的位数。对于下面每个DRAM，确定2的幂数的阵列维数，使得max(br, bc)最小，max(br, bc)是对阵列的行寻址或列寻址所需的位数中较大的值
目标：使纵横比最小，使地址位数最小，数组越接近正方形，地址位数越少
组织 | r | c | br | bc | Max(br,bc)
16×1 | 4 | 4 | 2 | 2 | 2
16×4 | 4 | 4 | 2 | 2 | 2
128×8 | 16 | 8 | 4 | 3 | 4
512×4 | 32 | 16 | 5 | 4 | 5
1024×4 | 32 | 32 | 5 | 5 | 5

## Slide 25: Enhanced DRAMs
Basic DRAM cell has not changed since its invention in 1966.
  Commercialized by Intel in 1970.
DRAM cores with better interface logic and faster I/O :
  Synchronous DRAM (SDRAM)
    Uses a conventional clock signal instead of asynchronous control
    Allows reuse of the row addresses (e.g., RAS, CAS, CAS, CAS)
  Double data-rate synchronous DRAM (DDR SDRAM)
    Double edge clocking sends two bits per cycle per pin
    Different types distinguished by size of small prefetch buffer:
      DDR (2 bits), DDR2 (4 bits), DDR3 (8 bits), DDR4 (16 bits)
    By 2010, standard for most server and desktop systems
    Intel Core i7 supports DDR3 and DDR4 SDRAM

## Slide 26: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Processors
and caches
Main Memory
Storage (SSD/HDD)
Notes: 主存是所有计算系统的关键组件，包括服务器平台、移动和嵌入式设备、桌面计算机以及传感器。它构成了任何计算平台的主要支柱之一，另外还有1) 处理单元(或计算单元)，它可以包括CPU内核、GPU内核、加速器或可重构设备; 2) 通信元素，它可以包括互连、网络接口和网络处理单元。

## Slide 27: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
GPUs
Notes: 主存是所有计算系统的关键组件，包括服务器平台、移动和嵌入式设备、桌面计算机以及传感器。它构成了任何计算平台的主要支柱之一，另外还有1) 处理单元(或计算单元)，它可以包括CPU内核、GPU内核、加速器或可重构设备; 2) 通信元素，它可以包括互连、网络接口和网络处理单元。

## Slide 28: The Main Memory System
Main memory is a critical component of all computing systems: server, mobile, embedded, desktop, sensor
Main memory system must scale (in size, technology, efficiency, cost, and management algorithms) to maintain performance growth and technology scaling benefits
Main Memory
Storage (SSD/HDD)
FPGAs
Notes: 主存是所有计算系统的关键组件，包括服务器平台、移动和嵌入式设备、桌面计算机以及传感器。它构成了任何计算平台的主要支柱之一，另外还有1) 处理单元(或计算单元)，它可以包括CPU内核、GPU内核、加速器或可重构设备; 2) 通信元素，它可以包括互连、网络接口和网络处理单元。
主存系统必须扩展（在大小、技术、效率、成本和管理算法方面）以保持性能增长和技术扩展优势。

## Slide 29: Three Key Systems Trends
1. Data access is a major bottleneck
  Applications are increasingly data hungry
2. Energy consumption is a key limiter
3. Data movement energy dominates compute
  Especially true for off-chip to on-chip movement

## Slide 30: Example: Capacity, Bandwidth & Latency
Chart: DRAM Improvement (log)
| 1999 | 2003 | 2006 | 2008 | 2011 | 2013 | 2014 | 2015 | 2016 | 2017
Capacity | 1 | 2 | 4 | 8 | 16 | 32 | 64 | 64 | 128 | 128
Bandwidth | 1 | 3.0075 | 6.015 | 8.015 | 10.0226 | 12.0301 | 14.0301 | 16.0376 | 18.0451 | 19.5489
Latency | 1 | 1 | 1.0435 | 1.1429 | 1.2121 | 1.2632 | 1.2521 | 1.275 | 1.2998 | 1.3187
128x
20x
1.3x
Memory latency remains almost constant
Notes: DRAM延迟几乎保持不变(即仅降低了30%，如图1所示)，同时缩放DRAM容量、带宽和延迟是有难度的，使其成为许多现代工作负载的重要性能瓶颈。

## Slide 31: The Need for More Memory Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Notes: 内存数据库，图处理，数据分析，数据中心工作负载，神经网络和消费者工作负载。

## Slide 32: DRAM Latency Is Critical for Performance
In-Memory Data Analytics
[Clapp+ (Intel), IISWC’15;
Awan+, BDCloud’15]
Datacenter Workloads [Kanev+ (Google), ISCA’15]
In-memory Databases
[Mao+, EuroSys’12; Clapp+ (Intel), IISWC’15]
Graph/Tree Processing
[Xu+, IISWC’12; Umuroglu+, FPL’15]
Long memory latency → performance bottleneck
Notes: 由于实时处理大量数据的需求不断增加，设计低延迟主存芯片变得越来越重要。

## Slide 33: Data Movement vs. Computation Energy
Dally, HiPEAC 2015
A memory access consumes ~1000X
the energy of a complex addition
Notes: 1000pJ=nJ
皮焦耳
纳焦耳

## Slide 34: Nonvolatile Memories
DRAM and SRAM are volatile memories
  Lose information if powered off.
Nonvolatile memories retain value even if powered off
  Read-only memory (ROM): programmed during production
  Programmable ROM (PROM): can be programmed once
  Eraseable PROM (EPROM): can be bulk erased (UV, X-Ray)
  Electrically eraseable PROM (EEPROM): electronic erase capability
  Flash memory: EEPROMs. with partial (block-level) erase capability
    Wears out after about 100,000 erasings
  3D XPoint (Intel Optane) & emerging NVMs
    New materials
Uses for Nonvolatile Memories
  Firmware programs stored in a ROM (BIOS, controllers for disks, network cards, graphics accelerators, security subsystems,…)
  Solid state disks (replace rotating disks in thumb drives, smart phones, mp3 players, tablets, laptops,…)
  Disk caches

## Slide 35
掩模式只读存储器(ROM)
在ROM的制作阶段，通过“掩模”工序将信息写到芯片内的。 容量为4×4位的电路情况。
有管子的读出为“0”，无管子的读出为“1”
A0
Vdd
D0
地
址
译
码
00
01
11
10
字选线0
字选线1
字选线3
字选线2
D1
D3
D2
A1

## Slide 36
字选线
Vcc
位线
熔丝
出厂时熔丝完好，表示存储元全为“1”。
写“0”时，通大电流将熔丝烧断。
可编程只读存储器(PROM)

## Slide 37
EPROM结构示意图

## Slide 38
快擦写可编程只读存储器 FLASH
Intel公司推出的一种半导体存储器
具有高密度、低成本、非易失性等特点的可读可写存储器。
可用电气方式快速擦写
既有DRAM的高集成度大容量的特点，又有可在线改写、断电信息不丢失的优点。
取代EPROM和EEPROM来保存主板等部件的BIOS，广泛应用于便携式计算机的PC卡存储器、USB电子盘、数码相机等。

## Slide 39: Emerging Nonvolatile Memories

## Slide 40: Resistive Random Access Memory（RRAM）
多层网络中的大量存储和计算导致了大量的矩阵乘累加操作。
ReRAM天然地适合进行乘累加操作。
因此，基于ReRAM的加速器被广泛用于DNN的部署。

## Slide 41: Data Movement in Computing Systems
  Comprises 41% of mobile system energy during web browsing*
  Costs 115x as much energy as an ADD operation**
Data movement dominates performance and is a major system energy bottleneck
*Reducing data Movement Energy via Online Data Clustering and Encoding (MICRO’16)
**Quantifying the energy cost of data movement for emerging smart phone workloads on mobile platforms (IISWC’14)
DRAM
Data Movement
GPU
CPU
CPU
SoC
L2
Video Decoder
Video Encoder
Audio
Display Engine
Processing-In-Memory proposes computing where it makes sense (where data resides)
Compute systems should be more data-centric

## Slide 42: Processing In-Memory (PIM)
Near-Data Processing or Processing In-Memory (PIM)
  Move computation closer to where the data resides
Logic layer
3D stacked DRAM
Memory module (DIMM)
Memory controller

## Slide 43: Application Trend of 3D

## Slide 44: UPMEM Processing-in-DRAM Engine
Processing in DRAM Engine
Includes standard DIMM modules, with a large number of DPU processors combined with DRAM chips.
Replaces standard DIMMs
  DDR4 R-DIMM modules
    8GB+128 DPUs (16 PIM chips)
    Standard 2x-nm DRAM process
  Large amounts of compute & memory bandwidth
https://www.anandtech.com/show/14750/hot-chips-31-analysis-inmemory-processing-by-upmem
https://www.upmem.com/video-upmem-presenting-its-true-processing-in-memory-solution-hot-chips-2019/
CPU
(x86, ARM, RV…)
DDR
Data bus
Notes: UPMEM PIM体系结构是第一个真实世界中公开可用的PIM体系结构。
这个PNM系统由一个简单的处理器(称为DRAM处理单元，DPU)组成，实现在一个DRAM芯片的每个bank旁边。DPU具有高带宽、低延迟、低能耗的访问其对应库中的所有数据的能力。

## Slide 45: DPU System

## Slide 46: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 47: Storage Technologies
Magnetic Disks
Store on magnetic medium
Electromechanical access
Nonvolatile (Flash) Memory
Store as persistent charge
Implemented with 3-D structure
  100+ levels of cells
  3 bits data per cell

## Slide 48: What’s Inside A Disk Drive?
主轴：固定速率旋转
磁头臂：操作硬盘磁头在介质表面进行数据读写
驱动电机：驱动
磁盘臂定位
盘片：表面覆盖
磁性材料
Electronics
(including a
processor
and memory!)
SCSI
接口

## Slide 49: 磁盘结构
磁盘由一组盘片（platers）构成，每个盘片有两个存储面（surface）
每个盘面由一系列同心圆磁道（track）组成
每个磁道由一系列扇区（sectors）组成，扇区之间由间隙（gaps）分隔
Spindle
主轴
Surface
面
Tracks
磁道
磁道 k
Sectors
扇区
间隙

## Slide 50: Disk Geometry (Muliple-Platter View)
Surface 0
面 0
Surface 1
Surface 2
Surface 3
Surface 4
Surface 5
Cylinder k
柱面 k
Spindle
主轴
Platter 0
盘片 0
Platter 1
盘片1
Platter 2
盘片 2
柱面(cylinder)：所有盘片表面上到主轴中心的距离相等的磁道的集合
  示例：柱面k是3个盘片、6个面上6个磁道k的集合
Notes: Cylinder： 柱面

## Slide 51: Computing Disk Capacity
示例：
  512 bytes/sector
  300 sectors/track (on average)
  20,000 tracks/surface
  2 surfaces/platter
  5 platters/disk
= 30,720,000,000
= 30.72 GB

## Slide 52: 练习题 计算磁盘容量
磁盘有4个盘片，2000个柱面，每条磁道平均3000个扇区，每扇区512字节
= 24,000,000,000
= 24 GB
磁盘有2个盘片，10000个柱面，每条磁道平均400个扇区，每扇区512字节
= 8,192,000,000
= 8.192 GB

## Slide 53: Disk Capacity
Capacity(容量）: maximum number of bits that can be stored.
  Vendors express capacity in units of gigabytes (GB), where 1 GB = 109 Bytes.
Capacity is determined by these technology factors:
  记录密度(Recording density (位/英寸))： 磁道一英寸的段中可以放入的位数
  磁道密度(Track density (道/英寸))： 从盘片中心出发半径上一英寸的段内可以有的有磁道数
  面密度(Areal density (位/平方英寸))：
  记录密度与磁道密度的乘积
Tracks

## Slide 54: Recording zones
初期：每个磁道分为数目相同的扇区，扇区数量由最靠内的磁道能记录的扇区数决定
  缺点：越靠外，扇区间隔越大
当前：柱面集合分割为不相交的子集合—记录区(recording zone)
每个记录区包含一组连续的柱面
一个区中每个柱面中的每条磁道都有相同数量的扇区
扇区数量由该区中最里面的磁道所能包含的扇区数量决定
Spindle
…

## Slide 55: Disk Operation (Single-Platter View)
The disk surface
spins at a fixed
rotational rate
seek: by moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
spindle
寻道：通过传动臂将磁头定位在指定磁道上

## Slide 56: Disk Operation (Multi-Platter View)
Arm
Read/write heads
move in unison
from cylinder to cylinder
Spindle
读/写：读写头感知(读该位)或修改(写该位)磁道上的位值

## Slide 57: Disk Structure - top view of single platter
Tracks divided into sectors
Surface organized into tracks
Notes: Goal:Show the inefficeincy of current disk requests
.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 58: Disk Access
Head in position above a track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 59: Disk Access
Rotation is counter-clockwise
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 60: Disk Access – Read
About to read blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 61: Disk Access – Read
After BLUE read
After reading blue sector
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 62: Disk Access – Read
After BLUE read
Red request scheduled next
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 63: Disk Access – Seek
After BLUE read
Seek for RED
Seek to red’s track
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 64: Disk Access – Rotational Latency
After BLUE read
Seek for RED
Rotational latency
Wait for red sector to rotate around
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 65: Disk Access – Read
After BLUE read
Seek for RED
Rotational latency
After RED read
Complete read of red
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 66: Disk Access – Service Time Components
After BLUE read
Seek for RED
Rotational latency
After RED read
Data transfer
Seek
Rotational
latency
Data transfer
Notes: Goal:
Show the inefficeincy of current disk requests.
Conveyed Ideas:
Rotational latency is wasted time that can be used to service tasks
Background Information:
None.
Slide Background:
None.
Kill text and arrows

## Slide 67: 扇区访问时间
扇区访问时间由三部分组成：寻道时间、旋转时间和传送时间
  Taccess = Tavg seek + Tavg rotation + Tavg transfer
寻道时间Tavg seek ：
  移动传动臂将读/写头定位到包含目标扇区磁道上所需的时间
  平均寻道时间为3~9ms
旋转时间：
  驱动器等待目标扇区的第一位旋转到读/写头下的时间
  最大旋转延迟为等待一整圈：
  平均旋转延迟为最大旋转延迟一半：
  典型磁盘转速为7200RPM或15K RPM
传送时间：
  当目标扇区的第一个位位于读/写头下时，驱动器读或写该扇区的时间
  一个扇区以秒为单位的平均传送时间为：
time for one rotation (in minutes)
fraction of a rotation to be read

## Slide 68: 练习题
估算磁盘扇区访问时间(ms)
  旋转速率：15000RPM
  平均寻道时间：8ms
  每条磁道的平均扇区数：500
访问时间估算：
  平均旋转延迟：
  平均传送时间：
  总访问延迟：

## Slide 69: 扇区访问时间示例
访问延迟
  磁盘大约10ms的访问延迟，主要是寻道延迟和旋转延迟
  访问扇区第一个位用时很长，访问其他字节时间极少
  SRAM中一个cache line(64字节)访问时间为4ns
  DRAM访问时间为60ns；
访问512字节大小
  SRAM读512个字节大小的块时间为256ns
  DRAM为4000ns
  磁盘访问时间为10ms
  是SRAM的40000倍，是DRAM的2500倍
Chart: 磁盘访问延迟
| 平均寻道延迟 | 平均旋转延迟 | 平均传送延迟
延迟(ms) | 9 | 4 | 0.02

## Slide 70: I/O Bus
CPU chip
主存
I/O
桥接器
总线接口
ALU
寄存器文件
系统总线
内存总线
磁盘控制器
图形适配器
USB控制器
鼠标
键盘
监视器
Disk
I/O总线
主机总线适配器
固态
硬盘
磁盘
网络适配器等其他设备扩展插槽

## Slide 71: 访问磁盘——从磁盘读数据(1)
主存
I/O
桥接器
总线接口
ALU
寄存器文件
系统总线
内存总线
磁盘控制器
图形适配器
USB控制器
鼠标
键盘
监视器
Disk
I/O总线
主机总线适配器
固态
硬盘
磁盘
网络适配器等其他设备扩展插槽
CPU使用内存映射I/O技术向I/O设备发射命令。
CPU通过将命令、逻辑块号和目的内存地址写到与磁盘相关联的内存映射地址，发起一个磁盘读

## Slide 72: 访问磁盘——从磁盘读数据(2)
主存
I/O
桥接器
总线接口
ALU
寄存器文件
系统总线
内存总线
磁盘控制器
图形适配器
USB控制器
鼠标
键盘
监视器
Disk
I/O总线
主机总线适配器
固态
硬盘
磁盘
网络适配器等其他设备扩展插槽
磁盘控制器收到来自CPU的读命令后，将逻辑块号翻译成一个扇区地址，磁盘控制器读扇区内容，并通过DMA方式将扇区内容直接传送到主存，不需要CPU的干涉

## Slide 73: 访问磁盘——从磁盘读数据(3)
主存
I/O
桥接器
总线接口
ALU
寄存器文件
系统总线
内存总线
磁盘控制器
图形适配器
USB控制器
鼠标
键盘
监视器
Disk
I/O总线
主机总线适配器
固态
硬盘
磁盘
网络适配器等其他设备扩展插槽
当DMA传送完成时，磁盘控制器用中断的方式通知CPU，CPU暂停当前工作，跳转到一个操作系统例程，这个程序会记录下I/O已完成，然后将控制返回到CPU被中断的地方

## Slide 74: 磁盘逻辑块
现代磁盘使用复杂扇区的简单抽象视图：
  扇区大小的逻辑块序列0,1,2,…,B-1对应B个扇区
逻辑块与物理块映射
  使用磁盘中固件设备——磁盘控制器
  维护逻辑块号和物理磁盘扇区(面-磁道-扇区)之间的映射关系
操作系统I/O操作(如读一个扇区到主存)过程：
  发送读某个逻辑块号命令到磁盘控制器
  控制器固件执行一个快速表查找，将一个逻辑块号翻译成一个(盘面-磁道-扇区)三元组，唯一地标识对应的物理扇区
  控制器解释此三元组，将读/写头移动到相应的柱面，等待扇区移动到读/写头下，将读/写头感知到的位放到控制器上的小缓冲区中，将缓冲区中的数据复制到主存
  格式化的容量比物理容量小

## Slide 75: 硬盘新技术：速度&容量
多读写臂技术
叠瓦式磁记录
（SMR）技术

## Slide 76: 固态硬盘
固态硬盘是一种基于闪存的存储技术，SSD封装为M.2、PCIe、SATA、USB等接口插到I/O总线上
Intel Optane系列SSD
SATA接口SSD
M.2接口SSD
PCIe接口SSD

## Slide 77: 固态硬盘逻辑结构
页大小：512KB~4KB, 块: 32~128页
数据以页为单位读写
页所属的块被整个擦除后才能写该页
块磨损：经过大约100000次重复写后，块磨损坏，不可用
闪存翻译层
I/O总线
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
闪存
固态硬盘(Solid State Disk, SSD)
读写逻辑磁盘块

## Slide 78: SSD Performance Characteristics
Benchmark of Samsung 940 EVO Plus
Sequential access faster than random access
  Common theme in the memory hierarchy
Random writes are somewhat slower
  Erasing a block takes a long time (~1 ms).
  Modifying a block page requires all other pages to be copied to new block.
  Flash translation layer allows accumulating series of small writes before doing block write.
Sequential read throughput 2,126 MB/s Sequential write tput 1,880 MB/s
Random read throughput 140 MB/s Random write tput 59 MB/s
https://ssd.userbenchmark.com/SpeedTest/711305/Samsung-SSD-970-EVO-Plus-250GB

## Slide 79: SSD Tradeoffs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    E.g. Samsung 940 EVO Plus guarantees 600 writes/byte of writes before they wear out
    Controller migrates data to minimize wear level
  In 2019, about 4 times more expensive per byte
    And, relative cost will keep dropping
Applications
  MP3 players, smart phones, laptops
  Increasingly common in desktops and servers

## Slide 80: 练习题 估算SSD寿命
假定SSD能够经得起128PB的写，根据工作负载估算SSD寿命
  顺序写最糟情况：以470MB/s速度持续写SSD
  随机写最糟情况：以303MB/s速度持续写SSD
  平均情况：以20GB/天速度写SSD
两种情况的估算寿命：
  顺序写最糟情况寿命：
  随机写最糟情况寿命：
  平均情况寿命：
  SSD的实际使用寿命通常都是大大超过官方标称值的

## Slide 81: The CPU-Memory Gap
The gap widens between DRAM, disk, and CPU speeds.
Chart: Year
| 1985 | 1990 | 1995 | 2000 | 2003 | 2005 | 2010 | 2015
Disk seek time | 75000000 | 28000000 | 10000000 | 8000000 | 6000000 | 5000000 | 3000000 | 3000000
SSD access time | 50000
DRAM access time | 200 | 100 | 70 | 60 | 55 | 50 | 40 | 20
SRAM access time | 150 | 35 | 15 | 3 | 2.5 | 2 | 1.5 | 1.3
CPU cycle time | 166 | 50 | 6 | 1.6 | 0.3 | 0.5 | 0.4 | 0.33
Effective CPU cycle time | 0.3 | 0.25 | 0.1 | 0.08
DRAM
CPU
SSD
Disk

## Slide 82: CPU Clock Rates
1985 1990 1995 2003 2005 2010 2015 2015:1985
CPU 80286 80386 Pentium P-4 Core 2 Core i7(n) Core i7(h)
Clock
rate (MHz) 6 20 150 3,300 2,000 2,500 3,000 500
Cycle
time (ns) 166 50 6 0.30 0.50 0.4 0.33 500
Cores 1 1 1 1 2 4 4 4
Effective
cycle 166 50 6 0.30 0.25 0.10 0.08 2,075
time (ns)
Inflection point in computer history
when designers hit the “Power Wall”
(n) Nehalem processor
(h) Haswell processor

## Slide 83: 练习题6.6 磁盘价格估算
基于2005-2015年数据，估算哪一年可以以$500的价格买到1PB的磁盘？
  1PB磁盘$500对应的单位存储价格为0.0005$/GB
  2005至2015年间价格变化相对稳定，作为基准参考价格
  取2010、2015两阶段平均价格递减倍数13.33
  估算后几个5年间磁盘单位容量价格，其中2025年约为0.00017 $/GB，即在2025年之前可能达到$500的价格买1PB磁盘的需求
 |  |  |  |  |  |  | 价格 | 容量(GB) | $/GB | 
 |  |  |  |  |  |  | 500 | 1000000 | 0.0005 | 
Year | 1985 | 1990 | 1995 | 2000 | 2005 | 2010 | 2015 | 2020 | 2025 | 2030
$/GB | 100000 | 8000 | 300 | 10 | 5 | 0.3 | 0.03 | 0.00225 | 0.00017 | 0.00001
递减倍数 |  | 12.50 | 26.67 | 30.00 | 2.00 | 16.67 | 10.00 |  |  | 
 |  |  |  |  |  | 平均倍数 | 13.33 |  |  | 

## Slide 84: Locality to the Rescue!
The key to bridging this CPU-Memory gap is a fundamental property of computer programs known as locality

## Slide 85: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 86: Locality
Principle of Locality: Programs tend to use data and instructions with addresses near or equal to those they have used recently
Temporal locality:
  Recently referenced items are likely to be referenced again in the near future
Spatial locality:
  Items with nearby addresses tend to be referenced close together in time

## Slide 87
作答
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality OR Temporal locality
[填空1]
[填空2]
[填空3]
[填空4]
填空题
4分

## Slide 88: Locality Example
Data references
  Reference array elements in succession (stride-1 reference pattern).
  Reference variable sum each iteration.
Instruction references
  Reference instructions in sequence.
  Cycle through loop repeatedly.
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Temporal locality
Spatial locality
Temporal locality

## Slide 89: Qualitative Estimates of Locality
Claim: Being able to look at code and get a qualitative sense of its locality is a key skill for a professional programmer.
Question: Does this function have good locality with respect to array a?
int sum_array_rows(int a[M][N])
{
int i, j, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
sum += a[i][j];
return sum;
}

## Slide 90: Locality Example
Question: Does this function have good locality with respect to array a?
int sum_array_cols(int a[M][N])
{
int i, j, sum = 0;
for (j = 0; j < N; j++)
for (i = 0; i < M; i++)
sum += a[i][j];
return sum;
}
Answer: no, unless…
M is very small

## Slide 91: 多维数组引用局部性
多维数组行优化顺序与列优化顺序具有不同的局部性
int sumarrayrows(int a[M][N]){
int i,j,sum=0;
for (i=0;i<M;i++)
for (j=0;j<N;j++)
sum+=a[i][j];
return sum;
}
int sumarraycols(int a[M][N]){
int i,j,sum=0;
for (j=0;j<N;j++)
for (i=0;i<M;i++)
sum+=a[i][j];
return sum;
}
a00
a01
a02
a03
a04
a05
a0 M-1
…
a00
a10
a20
a30
a40
a50
…
aN-1 0
a00
a01
a02
a03
a04
a05
a0 M-1
…
a00
a10
a20
a30
a40
a50
…
aN-1 0
Cache line
Cache line
Cache line
Notes: #include "vec.h"
#include "stdio.h"
#include "stdlib.h"
#include "time.h"
#include "Rdtsc.h" /* startTimer, stopTimer */
#define M 64
#define N 1024
int sumarrayrows(int a[M][N]){
int i,j,sum=0;
for (i=0;i<M;i++)
for (j=0;j<N;j++)
sum+=a[i][j];
return sum;
}
int sumarraycols(int a[M][N]){
int i,j,sum=0;
for (j=0;j<N;j++)
for (i=0;i<M;i++)
sum+=a[i][j];
return sum;
}
int main(){
uint64_t timer;
double cycleselem;
int i,j,sumArray=0;
int a[M][N];
for (i=0;i<M;i++)
for (j=0;j<N;j++)
a[i][j]=1;
startTimer(&timer);
sumArray=sumarrayrows(a);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("sumarray by rows is %ld, cycles_per_elem:%4.1lf\n",sumArray,cycleselem);
startTimer(&timer);
sumArray=sumarraycols(a);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("sumarray by cols is %ld, cycles_per_elem:%4.1lf\n",sumArray,cycleselem);
return 0;
}

## Slide 92: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}
Answer: make j the inner loop

## Slide 93
层次结构：
  存储器系统(memory system)：具有不同容量、成本和访问时间的层次结构
  高速缓存储器(cache memory)：靠近CPU的小的、快速的高速缓存存储器作为一部分存储在相对慢速的主存储器中数据和指令的缓冲区
  主存储器(main memory)：主存储器缓存存储在容量较大的、慢速磁盘上的数据
寄存器
高速缓存
内存
flash memory/PCM闪存
磁盘
磁带
存储集群

## Slide 94: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 95: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 96: Storage Trends
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 880 100 30 1 0.1 0.06 0.02 44,000
access (ns) 200 100 70 60 50 40 20 10
typical size (MB) 0.256 4 16 64 2,000 8,000 16.000 62,500
DRAM
SRAM
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/GB 100,000 8,000 300 10 5 0.3 0.03 3,333,333
access (ms) 75 28 10 8 5 3 3 25
typical size (GB) 0.01 0.16 1 20 160 1,500 3,000 300,000
Disk
Metric 1985 1990 1995 2000 2005 2010 2015 2015:1985
$/MB 2,900 320 256 100 75 60 25 116
access (ns) 150 35 15 3 2 1.5 1.3 115

## Slide 97: Example Memory Hierarchy
Regs
L1 cache
(SRAM)
Main memory
(DRAM)
Local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
Remote secondary storage
(e.g., Web servers)
Local disks hold files retrieved from disks
on remote servers
L2 cache
(SRAM)
L1 cache holds cache lines retrieved from the L2 cache.
CPU registers hold words retrieved from the L1 cache.
L2 cache holds cache lines
retrieved from L3 cache
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
Main memory holds disk blocks retrieved from local disks.

## Slide 98: 存储技术趋势

## Slide 99: Caches
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device.
Fundamental idea of a memory hierarchy:
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1.
Why do memory hierarchies work?
  Because of locality, programs tend to access the data at level k more often than they access the data at level k+1.
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit.
Big Idea (Ideal): The memory hierarchy creates a large pool of storage that costs as much as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top.

## Slide 100: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10

## Slide 101: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!

## Slide 102: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy: determines where b goes
Replacement policy: determines which block gets evicted (victim)

## Slide 103: General Caching Concepts: Types of Cache Misses
强制不命中(compulsory miss)或冷不命中(cold miss)
  缓存为空时产生的不命中，是暂时事件，缓存暖身(warm up)之后消失
冲突不命中(Conflict miss)
  缓存放置策略(placement policy)：通常将第k+1层的某个块限制放在第k层块的一个小的子集中(有时是一个块)
    例：第k+1层的块i必须放置在第k层的块(i mod 4)中
  冲突不命中(Conflict misses)指在限制性的放置策略中缓存足够 大，能够保存被引用的数据对象，但因为这些对象会映射到同一个缓存块，缓存会一直不命中
    例：程序请求块0, 8, 0, 8, 0, 8, ... ，在第k层的缓存中，对这两个块的每次引用都会不命中
容量(Capacity miss)
  当工作集大小超过缓存大小时产生的不命中

## Slide 104: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 105: 练习题
假设1MB文件由512字节的逻辑块组成，存储在具有如下特性的磁盘驱动器上：
  旋转速率：10,000RPM, 平均寻道时间：5ms
  每条磁道的平均扇区数：1000, 表面：4
  扇区大小：512字节
  假设程序顺序地读文件的逻辑块，一个接一个，将读/写头定位到第一块上的时间是
    最好的情况：给定逻辑块到磁盘扇区的最好的可能映射，估计读文件需要的最优时间(ms)
    随机的情况：如果块是随机地映射到磁盘扇区的，估计读文件需要的时间
答：
  1MB/512B=2000块，2000块/1000=2圈
  连接读取不用移动读/写头，定位到第一个扇区后，需要磁盘旋转2圈读取所有2000个块，总时间为：
  随机情况：块被随机映射到扇区上，读2000个块中的每一块都需要ms，读文件总时间为：
  随机与最好情况总时间比为：16000：20=800：1

## Slide 106: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.