## Slide 1
存储器层次结构（2）
王晶
jwang@ruc.edu.cn，信息楼124
2023年12月

## Slide 2: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 3: 局部性原理
局部性(locality)：倾向于引用邻近于其他最近引用过的数据项的数据项，或者最近引用过的数据项本身
局部性原理(principle of locality)：数据局部性的倾向性称为局部性原理
局部性的两种形式：
    时间局部性(temporal locality)：被引用过的内存位置很可能在不远的将来再被多次引用
    空间局部性(spatial locality)：一个内存位置被引用了一次，程序很可能在不远的将来引用附近的一个内存位置

## Slide 4: 多维数组引用局部性
多维数组行优化顺序与列优化顺序具有不同的局部性
int sumarrayrows(int a[M][N]){
int i,j,sum=0;
for (i=0;i<M;i++)
for (j=0;j<N;j++)
sum+=a[i][j];
return sum;
}
int sumarraycols(int a[M][N]){
int i,j,sum=0;
for (j=0;j<N;j++)
for (i=0;i<M;i++)
sum+=a[i][j];
return sum;
}
a00
a01
a02
a03
a04
a05
a0 M-1
…
a00
a10
a20
a30
a40
a50
…
aN-1 0
a00
a01
a02
a03
a04
a05
a0 M-1
…
a00
a10
a20
a30
a40
a50
…
aN-1 0
Cache line
Cache line
Cache line
Notes: #include "vec.h"
#include "stdio.h"
#include "stdlib.h"
#include "time.h"
#include "Rdtsc.h" /* startTimer, stopTimer */
#define M 64
#define N 1024
int sumarrayrows(int a[M][N]){
int i,j,sum=0;
for (i=0;i<M;i++)
for (j=0;j<N;j++)
sum+=a[i][j];
return sum;
}
int sumarraycols(int a[M][N]){
int i,j,sum=0;
for (j=0;j<N;j++)
for (i=0;i<M;i++)
sum+=a[i][j];
return sum;
}
int main(){
uint64_t timer;
double cycleselem;
int i,j,sumArray=0;
int a[M][N];
for (i=0;i<M;i++)
for (j=0;j<N;j++)
a[i][j]=1;
startTimer(&timer);
sumArray=sumarrayrows(a);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("sumarray by rows is %ld, cycles_per_elem:%4.1lf\n",sumArray,cycleselem);
startTimer(&timer);
sumArray=sumarraycols(a);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("sumarray by cols is %ld, cycles_per_elem:%4.1lf\n",sumArray,cycleselem);
return 0;
}

## Slide 5: Locality Example
Question: Can you permute the loops so that the function scans the 3-d array a with a stride-1 reference pattern (and thus has good spatial locality)?
int sum_array_3d(int a[M][N][N])
{
int i, j, k, sum = 0;
for (i = 0; i < M; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
sum += a[k][i][j];
return sum;
}
Answer: make j the inner loop

## Slide 6: 取指令的局部性
程序指令放在内存中，CPU需要读出指令
For循环体内的指令按照连续的内存顺序执行
  循环有良好的空间局部性
  循环体被执行多次，循环有良好的时间局部性
代码执行时不能被修改，程序执行时CPU只从内存中读指令，很少重写或修改指令
结论：行访问比列访问方式的指令局部性略高

## Slide 7: Summary
The speed gap between CPU, memory and mass storage continues to widen.
Well-written programs exhibit a property called locality.
Memory hierarchies based on caching close the gap by exploiting locality.

## Slide 8: Memory Hierarchies
Some fundamental and enduring properties of hardware and software:
  Fast storage technologies cost more per byte, have less capacity, and require more power (heat!).
  The gap between CPU and main memory speed is widening.
  Well-written programs tend to exhibit good locality.
These fundamental properties complement each other beautifully.
They suggest an approach for organizing memory and storage systems known as a memory hierarchy.

## Slide 9: 存储器层次结构
寄存器
L1 cache
(SRAM)
主存
(DRAM)
本地二级存储
(本地磁盘)
更大
更慢
每字节成本更低
的存储设备
远程二级存储
(分布式文件系统、web服务器)
本地磁盘保存从远程网络服务器磁盘取出的文件
L2 cache
(SRAM)
L1 cache保存从L2 cache取出的缓存行
CPU寄存器保存从L1 cache取出的机器字
L0:
L1:
L2:
L3:
L4:
L5:
更小
更快
每字节成本更高
的存储设备
L3 cache
(SRAM)
L3 cache holds cache lines
retrieved from main memory.
L6:
主存保存从本地磁盘取出的磁盘块
L2 cache保存从L3 cache取出的缓存行
L3 cache保存从主存取出的缓存行

## Slide 10: Today
The memory abstraction
RAM : main memory building block
Storage technologies and trends
Locality of reference
Caching in the memory hierarchy

## Slide 11: Examples of Caching in the Mem. Hierarchy
Hardware MMU
0
On-Chip TLB
Address translations
TLB
Web browser
10,000,000
Local disk
Web pages
Browser cache
Web cache
Network buffer cache
Buffer cache
Virtual Memory
L2 cache
L1 cache
Registers
Cache Type
Web pages
Parts of files
Parts of files
4-KB pages
64-byte blocks
64-byte blocks
4-8 bytes words
What is Cached?
Web proxy server
1,000,000,000
Remote server disks
OS
100
Main memory
Hardware
4
On-Chip L1
Hardware
10
On-Chip L2
NFS client
10,000,000
Local disk
Hardware + OS
100
Main memory
Compiler
0
CPU core
Managed By
Latency (cycles)
Where is it Cached?
Disk cache
Disk sectors
Disk controller
100,000
Disk firmware

## Slide 12: Caches
高速缓存(cache)：是一个小而快速的存储设备，作为存储在更大、更慢下一级设备中的数据对象的缓冲区域
缓存(caching)：使用高速缓存的过程
存储器层次的中心思想：
  对于每个k，位于k层的更快更小的存储设备作为位于k+1层的更大更慢存储设备的缓存
存储层次的工作原理：
  Power law(80/20原则)， k+1层数据中部分数据属于频繁访问的热数据，大部分数据属于不频繁访问的冷数据
  程序局部性特点倾向于访问k层的数据，速度快于k+1层数据访问
  k+1层数据访问更慢，但可以提供更大的容量
重要思想: 存储层次创建一个大的存储池，成本接近底层存储，性能接近上层存储

## Slide 13: General Cache Concepts
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Larger, slower, cheaper memory
viewed as partitioned into “blocks”
Data is copied in block-sized transfer units
Smaller, faster, more expensive
memory caches a subset of
the blocks
4
4
4
10
10
10
Cache是一种小容量高速缓冲存储器，它由SRAM组成。
Cache直接制作在CPU芯片内，速度几乎与CPU一样快。
程序运行时，CPU使用的一部分数据/指令会预先成批拷贝在Cache中，Cache的内容是主存储器中部分内容的映象。
当CPU需要从内存读(写)数据或指令时，先检查Cache，若有，就直接从Cache中读取，而不用访问主存储器。

## Slide 14: General Cache Concepts: Hit
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 14
14
Block b is in cache:
Hit!（命中）
问：若主存的访问时间为60n秒，CACHE的访问时间为10n秒，在命中率为90﹪时，CPU访存的平均时间为多少？
解：
10ns×90﹪ + 60ns×10﹪
= 15ns

## Slide 15: General Cache Concepts: Miss
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
8
9
14
3
Cache
Memory
Data in block b is needed
Request: 12
Block b is not in cache:
Miss!（缺失）
Block b is fetched from
memory
Request: 12
12
12
12
Block b is stored in cache
Placement policy放置: determines where b goes
Replacement policy替换: determines which block gets evicted (victim)

## Slide 16
Cache 的操作过程
若被访问信息不在cache中，称为缺失或失靶(miss)
若被访问信息在cache中，称为命中(hit)

## Slide 17: Types of Cache Misses
强制缺失(compulsory miss)或冷缺失(cold miss)
  缓存为空时产生的缺失，是暂时事件，缓存暖身(warm up)之后消失
冲突缺失(Conflict miss)
  缓存放置策略(placement policy)：通常将第k+1层的某个块限制放在第k层块的一个小的子集中(有时是一个块)
    例：第k+1层的块i必须放置在第k层的块(i mod 4)中
  冲突缺失(Conflict misses)指在限制性的放置策略中缓存足够 大，能够保存被引用的数据对象，但因为这些对象会映射到同一个缓存块，缓存会一直不命中
    例：程序请求块0, 8, 0, 8, 0, 8, ... ，在第k层的缓存中，对这两个块的每次引用都会失效
容量缺失(Capacity miss)
  当工作集大小超过缓存大小时产生的不命中

## Slide 18: Cache Memories
Cache memories are small, fast SRAM-based memories managed automatically in hardware
  Hold frequently accessed blocks of main memory
CPU looks first for data in cache
Typical system structure:
Main
memory
I/O
bridge
Bus interface
ALU
Register file
CPU chip
System bus
Memory bus
Cache
memory

## Slide 19: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 20: Cache的块
在存储系统中,把Cache和主存储器都划分成相同大小的块。
例如：设主存：64KB Cache：1KB 块大小：32B
所以：主存分为2K个块
CACHE可容纳32个块
映像方式
  直接映象及其变换
  全相联映象及其变换
  组相联映象及其变换

## Slide 21
0﹟块
1﹟块
2﹟块
3﹟块
Cache
2﹟块
0﹟块
1﹟块
3﹟块
4﹟块
5﹟块
6﹟块
7﹟块
15﹟块
13﹟块
14﹟块
： ：
0﹟区
1﹟区
3﹟区
主存
12﹟块
Cache的块与主存一个区中的块一一对应
直接映象方式示意图

## Slide 22: 直接映射高速缓存
地址 (十进制) | 地址位 |  |  | 块号 (十进制）
 | 标记 (t=1) | 索引 (s=2) | 偏移 (b=1) | 
0 | 0 | 00 | 0 | 0
1 | 0 | 00 | 1 | 0
2 | 0 | 01 | 0 | 1
3 | 0 | 01 | 1 | 1
4 | 0 | 10 | 0 | 2
5 | 0 | 10 | 1 | 2
6 | 0 | 11 | 0 | 3
7 | 0 | 11 | 1 | 3
8 | 1 | 00 | 0 | 4
9 | 1 | 00 | 1 | 4
10 | 1 | 01 | 0 | 5
11 | 1 | 01 | 1 | 5
12 | 1 | 10 | 0 | 6
13 | 1 | 10 | 1 | 6
14 | 1 | 11 | 0 | 7
15 | 1 | 11 | 1 | 7
假设直接映射高速缓存(S,E,B,m)=(4,1,2,4)：
  高速缓存有4个组
  每组1行
  每个块2字节
  地址位是4位
地址映射
  标记位和索引位连起来唯一标识内存中的每个块
  有8个内存块，4个高速缓存组，有相同组索引的多个块映射到一个高速缓存组
  映射到同一个高速缓存组的块由标记唯一地址标识

## Slide 23: 直接映象方式
字块2c+1
字块7
字块5
字块2c
字块3
字块1
字块0
…
主存储体
字块 1
标记
字块 0
标记
字块 2c－1
标记
Cache存储体
t位
0
1
2c－1
…
字块
字块地址
主存字
块标记
t 位
s 位
b 位
主存地址
*
Cache
内地址
每个缓存块 i 可以和 若干 个 主存块 对应
每个主存块 j 只能和 一 个 缓存块 对应
i = j mod n
字块2
字块6
字块14
字块13
字块12
字块10
字块9
字块11
字块15
字块8
字块4
字块0
字块 0
字块12

## Slide 24: Cache缓存示例
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
0
v
011
010
0
v
101
100
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
1.读地址0的字

## Slide 25: Cache缓存示例
m[1]
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[0]
0
v
011
010
0
v
101
100
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
1.读地址0的字

## Slide 26: Cache缓存示例
m[1]
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[0]
0
v
011
010
0
v
101
100
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
2.读地址1的字

## Slide 27: Cache缓存示例
m[1]
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[0]
0
v
011
010
0
v
101
100
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
3.读地址13的字

## Slide 28: Cache缓存示例
m[1]
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[0]
0
v
011
010
m[13]
1
v
101
100
m[12]
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
3.读地址13的字

## Slide 29: Cache缓存示例
m[1]
1
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[0]
0
v
011
010
m[13]
0
v
101
100
m[12]
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
4.读地址8的字

## Slide 30: Cache缓存示例
m[9]
1
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[8]
0
v
011
010
m[13]
0
v
101
100
m[12]
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
4.读地址8的字

## Slide 31: Cache缓存示例
m[9]
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[8]
0
v
011
010
m[13]
0
v
101
100
m[12]
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
5.读地址0的字

## Slide 32: Cache缓存示例
m[1]
0
v
00
0
00
0
0
00
1
0
01
0
0
01
1
0
10
0
0
10
1
0
11
0
0
11
1
01
10
11
1
00
0
1
00
1
1
01
0
1
01
1
1
10
0
1
10
1
1
11
0
1
11
1
Cache
Main-Memory
001
000
m[0]
0
v
011
010
m[13]
0
v
101
100
m[12]
0
v
111
110
m[1]
m[0]
m[3]
m[2]
m[5]
m[4]
m[7]
m[6]
m[9]
m[8]
m[11]
m[10]
m[13]
m[12]
m[15]
m[14]
5.读地址0的字

## Slide 33: Example: Direct Mapped Cache (E = 1)
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
1.直接映射高速缓存中的组选择
  通过组索引位(0…01)选择高速缓存中的组

## Slide 34: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
block offset
tag
1.直接映射高速缓存中的组选择
  通过组索引位(0…01)选择高速缓存中的组
2.直接映射高速缓存中的行匹配
  标记位为1，并且tag标记位与地址中的标记位相匹配
3.直接映射高速缓存中的字选择
    块偏移位(100)提供了所需要的字的第一个字节在cache block中的偏移地址

## Slide 35: Example: Direct Mapped Cache (E = 1)
Direct mapped: One line per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of int:
0
1
2
7
tag
v
3
6
5
4
match: assume yes = hit
valid? +
int (4 Bytes) is here
block offset
If tag doesn’t match: old line is evicted and replaced
  4.直接映射高速缓存不命中时的行替换
    如果不命中，从下一级存储器中取出请求的块，替换当前行

## Slide 36
[填空1]
[填空2]
[填空3]
[填空4]
[填空5]
作答
下面的访问如果命中填H，缺失填M
4-bit addresses (address space size M=16 bytes)
S=4 sets, E=1 Blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
v
Tag
Block
0
0
0
Set 0
Set 1
Set 2
Set 3
填空题
5分

## Slide 37: Direct-Mapped Cache Simulation
4-bit addresses (address space size M=16 bytes)
S=4 sets, E=1 Blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
x
t=1
s=2
b=1
xx
x
0
v
Tag
Block
0
0
0
miss
1
0
M[0-1]
hit
miss
1
0
M[6-7]
miss
1
1
M[8-9]
miss
0
M[0-1]
Set 0
Set 1
Set 2
Set 3
Notes: Pause at the end of this slide to consider that M[0] and M[8] have nothing to do with one another, but that they interfere with one anothers’ existences in the cache.

## Slide 38: 优缺点分析
直接映射
  优点:所需硬件简单,成本低；地址变换速度较快。
  缺点:块冲突概率很高；Cache利用率很低
抖动(trash)
  高速缓存反复地加载和驱逐相同的高速缓存块组

## Slide 39: 直接映射高速缓存中的冲突不命中
x |  |  |  | y |  |  | 
元素 | 地址 | 组索引 | 二进制地址 | 元素 | 地址 | 组索引 | 二进制地址
x[0] | 0 | 0 | 000000 | y[0] | 32 | 0 | 100000
x[1] | 4 | 0 | 000100 | y[1] | 36 | 0 | 100100
x[2] | 8 | 0 | 001000 | y[2] | 40 | 0 | 101000
x[3] | 12 | 0 | 001100 | y[3] | 44 | 0 | 101100
x[4] | 16 | 1 | 010000 | y[4] | 48 | 1 | 110000
x[5] | 20 | 1 | 010100 | y[5] | 52 | 1 | 110100
x[6] | 24 | 1 | 011000 | y[6] | 56 | 1 | 111000
x[7] | 28 | 1 | 011100 | y[7] | 60 | 1 | 111100
Float dotprod(float x[8], float y[8])
{
float sum=0.0;
int i;
for(i=0;i<8;i++)
sum+=x[i]*y[i];
return sum;
}
两个向量点积函数
  具有良好的空间局部性
  Cache命令率仍然较低
参数设置：
  浮点数4字节
  X加载到从0到32个字节连续内存
  Y加载到从32开始的连续内存
  一个块为16字节

## Slide 40: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[0]*y[0];
加载

## Slide 41: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[0]*y[0];
加载

## Slide 42: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[0]*y[0];
加载

## Slide 43: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[0]*y[0];
加载

## Slide 44: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[1]*y[1];
加载

## Slide 45: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[1]*y[1];
加载

## Slide 46: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[1]*y[1];
加载

## Slide 47: 内存与cache地址分布
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[1]*y[1];
加载

## Slide 48: Cache thrashing原因分析
抖动(trash)：高速缓存反复地加载和驱逐相同的高速缓存块组
原因：
  循环迭代处理语句中x[i]和y[i]内存块对应相同的cache组
  读取x[i]加载4个连续的浮点数到cache组
  读取y[i]加载4个连续的浮点数到相同的cache组，原x[i]数据块被cache驱逐
  读取x[i+1]需要重新加载4个连续的浮点数到cache组
  读取y[i+1] 重新驱逐已加载的4个连续的x[i+1]对应的浮点数
  周而复始…
  导致每个x[i]和y[i]产生一个cache miss

## Slide 49: 填充解决Cache thrashing
在数组尾部增加B字节填充，使x[i]和y[i]内存块对应不同的cache组
每4个浮点数只加载一次，命中3次，命中率为75%
s=1
Cache
11|10|01|00
0
v
111
110
11|10|01|00
11|10|01|00
11|10|01|00
s= 0
11|10|01|00
11|10|01|00
11|10|01|00
11|10|01|00
100
101
0
v
011
010
000
001
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
x[0]
x[1]
x[2]
x[3]
x[4]
x[5]
x[6]
x[7]
b
b
011111~011100
011011~011000
010111~010100
010011~010000
001111~001100
001011~001000
000111~000100
000011~000000
y[0]
y[1]
y[2]
y[3]
y[4]
y[5]
y[6]
y[7]
Main-Memory
sum+=x[0]*y[0];
加载
加载
011111~011100
011011~011000
010111~010100
010011~010000
B[0]
B[1]
B[2]
B[3]

## Slide 50: 优缺点分析
直接映射
  优点:所需硬件简单,成本低；地址变换速度较快。
  缺点:块冲突概率很高；Cache利用率很低
全相连？
主存 中的 任一块 可以映射到 缓存 中的 任一块
字块2m－1
字块2c－1
字块1
字块0
…
…
字块2c－1
字块1
字块0
…
标记
标记
标记
Cache 存储器
主存储器
字块0
  随着Cache容量的增加,查表速度很难提高且电路复杂，成本高

## Slide 51: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
find set
直接映射cache冲突不命中的根源为每个组只有一行(E=1)
组相关高速缓存(set associative cache)每个组都保存多于一个的高速缓存行，即1<E<C/B

## Slide 52: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
tag
1.组相联高速缓存中的组选择
  组索引位标识cache组
2.组相联高速缓存中的行匹配和字选择
  检查多个行的有效位和标记位，确定所请求的字是否在集合中

## Slide 53: E-way Set Associative Cache (Here: E = 2)
E = 2: Two lines per set
Assume: cache block size 8 bytes
t bits
0…01
100
Address of short int:
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
compare both
valid? +
match: yes = hit
block offset
short int (2 Bytes) is here
No match:
One line in set is selected for eviction and replacement
Replacement policies: random, least recently used (LRU), …

## Slide 54
作答
2-Way Set Associative Cache Simulation
4-bit addresses (M=16 bytes)
S=2 sets, E=2 blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
v
Tag
Block
0
0
0
Set 0
Set 1
[填空1]
[填空2]
[填空3]
[填空4]
[填空5]
填空题
5分

## Slide 55: 2-Way Set Associative Cache Simulation
4-bit addresses (M=16 bytes)
S=2 sets, E=2 blocks/set, B=2 bytes/block
Address trace (reads, one byte per read):
0 [00002],
1 [00012],
7 [01112],
8 [10002],
0 [00002]
xx
t=2
s=1
b=1
x
x
0
v
Tag
Block
0
0
0
miss
1
00
M[0-1]
hit
miss
1
01
M[6-7]
miss
1
10
M[8-9]
hit
Set 0
Set 1

## Slide 56: General Cache Organization (S, E, B)
E = 2e lines per set
S = 2s sets
set
line
0
1
2
B-1
tag
v
B = 2b bytes per cache block (the data)
Cache size:
C = S x E x B data bytes
valid bit

## Slide 57: Cache Read
E = 2e lines per set
S = 2s sets
0
1
2
B-1
tag
v
valid bit
B = 2b bytes per cache block (the data)
t bits
s bits
b bits
Address of word:
tag
set
index
block
offset
data begins at this offset
Locate set
Check if any line in set has matching tag
Yes + line valid: hit
Locate data starting at offset

## Slide 58: What about writes?
Multiple copies of data exist:
  L1, L2, L3, Main Memory, Disk
What to do on a write-hit?
  Write-through 写直达(write immediately to memory)
  Write-back 写回(defer write to memory until replacement of line)
    Each cache line needs a dirty bit (set if data has been written to)
What to do on a write-miss?
  Write-allocate写分配 (load into cache, update line in cache)
    Good if more writes to the location will follow
  No-write-allocate (writes straight to memory, does not load into cache)
Typical
  Write-through + No-write-allocate
  Write-back + Write-allocate（写回+写分配）
0
1
2
B-1
tag
d
B = 2b bytes
dirty bit
v
valid bit

## Slide 59: Practical Write-back Write-allocate
A write to address X is issued
If it is a hit
  Update the contents of block
  Set dirty bit to 1 (bit is sticky and only cleared on eviction)
If it is a miss
  Fetch block from memory (per a read miss)
  The perform the write operations (per a write hit)
If a line is evicted and dirty bit is set to 1
  The entire block of 2b bytes are written back to memory
  Dirty bit is cleared (set to 0)
  Line is replaced by new contents
0
1
2
B-1
tag
d
B = 2b bytes
dirty bit
v
valid bit

## Slide 60: Why Index Using Middle Bits?
S = 2s sets
Direct mapped: One line per set
Assume: cache block size 8 bytes
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
0
1
2
7
tag
v
3
6
5
4
t bits
0…01
100
Address of int:
find set
Standard Method:
Middle bit indexing
t bits
1…11
100
Address of int:
find set
Alternative Method:
High bit indexing

## Slide 61: Illustration of Indexing Approaches
64-byte memory
  6-bit addresses
16 byte, direct-mapped cache
Block size = 4. (Thus, 4 sets; why?)
2 bits tag, 2 bits index, 2 bits offset
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx
Notes: 16byte direct mapped $, 4B blocks -> must be 4 sets to account for all 16B of cache

## Slide 62: Middle Bit Indexing
Addresses of form TTSSBB
  TT Tag bits
  SS Set index bits
  BB Offset bits
Makes good use of spatial locality
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx

## Slide 63: High Bit Indexing
Addresses of form SSTTBB
  SS Set index bits
  TT Tag bits
  BB Offset bits
Program with high spatial locality would generate lots of conflicts
Set 0
Set 1
Set 2
Set 3
1111xx
1110xx
1101xx
1100xx
1011xx
1010xx
1001xx
1000xx
0111xx
0110xx
0101xx
0100xx
0011xx
0010xx
0001xx
0000xx
Notes: Go from block with set index bits 00 to 01, displace the line sitting in set 0 from the block with set index 00.

## Slide 64: Intel Core i7 Cache Hierarchy
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 0
Regs
L1
d-cache
L1
i-cache
L2 unified cache
Core 3
…
L3 unified cache
(shared by all cores)
Main memory
Processor package
L1 i-cache and d-cache:
  32 kB, 8-way,
  Access: 4 cycles
L2 unified cache:
  256 kB, 8-way,
  Access: 10 cycles
L3 unified cache:
  8 MB, 16-way,
  Access: 40-75 cycles
Block size: 64 bytes for all caches.

## Slide 65: Example: Core i7 L1 Data Cache
B = , b =
S = , s =
E = , e =
C =
Block offset: . bits
Set index: . bits
Tag: . bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x??
Set index: 0x??
Tag: 0x??
32 kB 8-way set associative
64 bytes/block
47 bit address range
Notes: B = 64 (2^6)
E = 8 (2^3)
S = 64 (2^6) [need to infer from B, E, and Cache Size]
Cache Size = 2^15 (32768)

## Slide 66: Example: Core i7 L1 Data Cache
B = 64, b=6
S = 64, s = 6
E = 8, e = 3
C = 64 x 64 x 8 = 32,768
Block offset: 6 bits
Set index: 6 bits
Tag: 35 bits
Stack Address: 0x00007f7262a1e010
Block offset: 0x10
Set index: 0x0
Tag: 0x7f7262a1e
32 kB 8-way set associative 64 bytes/block
47 bit address range
0000 0001 0000
Notes: 0x010 => 0000 0001 0000, say that it awkwardly segments the bits, but that’s ok

## Slide 67: Cache Performance Metrics
Miss Rate
  Fraction of memory references not found in cache (misses / accesses) = 1 – hit rate
  Typical numbers (in percentages):
    3-10% for L1
    can be quite small (e.g., < 1%) for L2, depending on size, etc.
Hit Time
  Time to deliver a line in the cache to the processor
    includes time to determine whether the line is in the cache
  Typical numbers:
    4 clock cycle for L1
    10 clock cycles for L2
Miss Penalty
  Additional time required because of a miss
    typically 50-200 cycles for main memory (Trend: increasing!)

## Slide 68: Let’s think about those numbers
Huge difference between a hit and a miss
  Could be 100x, if just L1 and main memory
Would you believe 99% hits is twice as good as 97%?
  Consider: cache hit time of 1 cycle miss penalty of 100 cycles
  Average access time:
  97% hits: 1 cycle + 0.03 * 100 cycles = 4 cycles
  99% hits: 1 cycle + 0.01 * 100 cycles = 2 cycles
This is why “miss rate” is used instead of “hit rate”

## Slide 69: Writing Cache Friendly Code
Make the common case go fast
  Focus on the inner loops of the core functions
Minimize the misses in the inner loops
  Repeated references to variables are good (temporal locality)重复引用相同变量的程序有良好的时间局部性
  频繁访问数据集的缓存级别：寄存器>L1 cache>L2 cache-L3 cache>内存
  Stride-1 reference patterns are good (spatial locality)步长为k的引用模式程序，步长越小，空间局部性越好
  CPU内存访问单位cache line(64字节)，步长越小，效率越高
  对于取指令而言，循环有好的时间和空间局部性，循环越小，循环迭代次数越多，局部性越好,简化循环体内代码结构
Key idea: Our qualitative notion of locality is quantified through our understanding of cache memories

## Slide 70
[填空1]
作答
void clear1(point *p, int n){
int i,j;
for (i=0;i<n;i++){
for (j=0;j<M;j++)
p[i].vel[j]=0;
for (j=0;j<M;j++)
p[i].acc[j]=0;
}
return;}
void clear2(point *p, int n){
int i,j;
for (i=0;i<n;i++){
for (j=0;j<M;j++){
p[i].vel[j]=0;
p[i].acc[j]=0;
} }
return;}
void clear3(point *p, int n){
int i,j;
for (j=0;j<M;j++){
for (i=0;i<n;i++)
p[i].vel[j]=0;
for (i=0;i<n;i++)
p[i].acc[j]=0;
}return;}
#define N 1024
#define M 256
typedef struct{
int vel[M];
int acc[M];
}point;
point p[N];
空间局部性排序
填空题
1分

## Slide 71: 练习题 分析三个函数的空间局部性
void clear1(point *p, int n){
int i,j;
for (i=0;i<n;i++){
for (j=0;j<M;j++)
p[i].vel[j]=0;
for (j=0;j<M;j++)
p[i].acc[j]=0;
}
return;}
void clear2(point *p, int n){
int i,j;
for (i=0;i<n;i++){
for (j=0;j<M;j++){
p[i].vel[j]=0;
p[i].acc[j]=0;
} }
return;}
void clear3(point *p, int n){
int i,j;
for (j=0;j<M;j++){
for (i=0;i<n;i++)
p[i].vel[j]=0;
for (i=0;i<n;i++)
p[i].acc[j]=0;
}return;}
#define N 1024
#define M 256
typedef struct{
int vel[M];
int acc[M];
}point;
point p[N];
Notes: #include "vec.h"
#include "stdio.h"
#include "stdlib.h"
#include "time.h"
#include "Rdtsc.h" /* startTimer, stopTimer */
#define N 1024
#define M 256
typedef struct{
int vel[M];
int acc[M];
}point;
point p[N];
void clear1(point *p, int n){
int i,j;
for (i=0;i<n;i++){
for (j=0;j<M;j++)
p[i].vel[j]=0;
for (j=0;j<M;j++)
p[i].acc[j]=0;
}
return;
}
void clear2(point *p, int n){
int i,j;
for (i=0;i<n;i++){
for (j=0;j<M;j++){
p[i].vel[j]=0;
p[i].acc[j]=0;
}
}
return;
}
void clear3(point *p, int n){
int i,j;
for (j=0;j<M;j++){
for (i=0;i<n;i++)
p[i].vel[j]=0;
for (i=0;i<n;i++)
p[i].acc[j]=0;
}
return;
}
int main(){
uint64_t timer;
double cycleselem;
startTimer(&timer);
clear1(p,N);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("clear1 function cycles_per_elem:%4.1lf\n",cycleselem);
startTimer(&timer);
clear2(p,N);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("clear2 function cycles_per_elem:%4.1lf\n",cycleselem);
startTimer(&timer);
clear3(p,N);
stopTimer(&timer);
cycleselem=((double)timer)/(M*N);
printf("clear3 function cycles_per_elem:%4.1lf\n",cycleselem);
return 0;
}

## Slide 72: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 73: The Memory Mountain
Read throughput (read bandwidth)
  Number of bytes read from memory per second (MB/s)
Memory mountain: Measured read throughput as a function of spatial and temporal locality.
  Compact way to characterize memory system performance.

## Slide 74: Memory Mountain Test Function
long data[MAXELEMS]; /* Global array to traverse */
/* test - Iterate over first "elems" elements of
* array “data” with stride of "stride", using
* using 4x4 loop unrolling.
*/
int test(int elems, int stride) {
long i, sx2=stride*2, sx3=stride*3, sx4=stride*4;
long acc0 = 0, acc1 = 0, acc2 = 0, acc3 = 0;
long length = elems, limit = length - sx4;
/* Combine 4 elements at a time */
for (i = 0; i < limit; i += sx4) {
acc0 = acc0 + data[i];
acc1 = acc1 + data[i+stride];
acc2 = acc2 + data[i+sx2];
acc3 = acc3 + data[i+sx3];
}
/* Finish any remaining elements */
for (; i < length; i++) {
acc0 = acc0 + data[i];
}
return ((acc0 + acc1) + (acc2 + acc3));
}
Call test() with many combinations of elems
and stride.
For each elems and stride:
1. Call test() once to warm up the caches.
2. Call test() again and measure the read throughput(MB/s)
mountain/mountain.c

## Slide 75: The Memory Mountain
Chart: Stride (x8 bytes)
| s1 | s2 | s3 | s4 | s5 | s6 | s7 | s8 | s9 | s10 | s11
128m | 8350 | 4750 | 3096 | 2286 | 1817 | 1512 | 1293 | 1131 | 1055 | 995 | 945 | 900
64m | 8352 | 4750 | 3092 | 2287 | 1816 | 1510 | 1291 | 1129 | 1051 | 989 | 938 | 894
32m | 8406 | 4787 | 3098 | 2289 | 1823 | 1512 | 1295 | 1133 | 1052 | 989 | 938 | 892
16m | 8556 | 4990 | 3204 | 2376 | 1891 | 1579 | 1356 | 1198 | 1127 | 1070 | 1028 | 994
8m | 8998 | 5447 | 3570 | 2643 | 2104 | 1743 | 1477 | 1300 | 1217 | 1158 | 1128 | 1096
4m | 11494 | 7921 | 5664 | 4319 | 3524 | 2991 | 2592 | 2298 | 2208 | 2148 | 2117 | 2077
2m | 12297 | 8417 | 5940 | 4573 | 3734 | 3174 | 2763 | 2446 | 2349 | 2272 | 2213 | 2160
1024k | 12422 | 8398 | 5971 | 4569 | 3740 | 3172 | 2756 | 2446 | 2351 | 2271 | 2209 | 2162
512k | 12432 | 8472 | 5950 | 4573 | 3726 | 3165 | 2758 | 2447 | 2341 | 2267 | 2210 | 2162
256k | 12564 | 10037 | 8679 | 7175 | 5915 | 5022 | 4345 | 3856 | 3895 | 3981 | 4001 | 4404
128k | 12711 | 10750 | 10271 | 8649 | 7525 | 6374 | 5482 | 4854 | 4901 | 4933 | 4917 | 4924
64k | 12687 | 10689 | 10208 | 8768 | 7570 | 6352 | 5460 | 4830 | 4885 | 4885 | 4823 | 4868
Core i7 Haswell
2.1 GHz
32 KB L1 d-cache
256 KB L2 cache
8 MB L3 cache
64 B block size
Slopes
of spatial locality
Ridges
of temporal locality
L1
Mem
L2
L3
Aggressive prefetching

## Slide 76: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 77: Matrix Multiplication Example
Description:
  Multiply N x N matrices
  Matrix elements are doubles (8 bytes)
  O(N3) total operations
  N reads per source element
  N values summed per destination
    but may be able to hold in register
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
Variable sum
held in register
matmult/mm.c

## Slide 78: Miss Rate Analysis for Matrix Multiply
Assume:
  Block size = 32B (big enough for four doubles)
  Matrix dimension (N) is very large
    Approximate 1/N as 0.0
  Cache is not even big enough to hold multiple rows
Analysis Method:
  Look at access pattern of inner loop
A
k
i
B
k
j
C
i
j
=
x

## Slide 79: Layout of C Arrays in Memory (review)
C arrays allocated in row-major order
  each row in contiguous memory locations
Stepping through columns in one row:
  for (i = 0; i < N; i++)
    sum += a[0][i];
  accesses successive elements
  if block size (B) > sizeof(aij) bytes, exploit spatial locality
    miss rate = sizeof(aij) / B
Stepping through rows in one column:
  for (i = 0; i < n; i++)
    sum += a[i][0];
  accesses distant elements
  no spatial locality!
    miss rate = 1 (i.e. 100%)

## Slide 80: Matrix Multiplication (ijk)
/* ijk */
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Column-
wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c

## Slide 81: Matrix Multiplication (jik)
/* jik */
for (j=0; j<n; j++) {
for (i=0; i<n; i++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum
}
}
A
B
C
(i,*)
(*,j)
(i,j)
Inner loop:
Row-wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  0.25 1.0 0.0
matmult/mm.c

## Slide 82: Matrix Multiplication (kij)
/* kij */
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c

## Slide 83: Matrix Multiplication (ikj)
/* ikj */
for (i=0; i<n; i++) {
for (k=0; k<n; k++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
A
B
C
(i,*)
(i,k)
(k,*)
Inner loop:
Row-wise
Row-wise
Fixed
Misses per inner loop iteration:
  A B C
  0.0 0.25 0.25
matmult/mm.c

## Slide 84: Matrix Multiplication (jki)
/* jki */
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Column-
wise
Column-
wise
Fixed
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c

## Slide 85: Matrix Multiplication (kji)
/* kji */
for (k=0; k<n; k++) {
for (j=0; j<n; j++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}
A
B
C
(*,j)
(k,j)
Inner loop:
(*,k)
Fixed
Column-
wise
Column-
wise
Misses per inner loop iteration:
  A B C
  1.0 0.0 1.0
matmult/mm.c

## Slide 86: Summary of Matrix Multiplication
ijk (& jik):
  2 loads, 0 stores
  misses/iter = 1.25
kij (& ikj):
  2 loads, 1 store
  misses/iter = 0.5
jki (& kji):
  2 loads, 1 store
  misses/iter = 2.0
for (i=0; i<n; i++) {
for (j=0; j<n; j++) {
sum = 0.0;
for (k=0; k<n; k++)
sum += a[i][k] * b[k][j];
c[i][j] = sum;
}
}
for (k=0; k<n; k++) {
for (i=0; i<n; i++) {
r = a[i][k];
for (j=0; j<n; j++)
c[i][j] += r * b[k][j];
}
}
for (j=0; j<n; j++) {
for (k=0; k<n; k++) {
r = b[k][j];
for (i=0; i<n; i++)
c[i][j] += a[i][k] * r;
}
}

## Slide 87: Core i7 Matrix Multiply Performance
Chart: Array size (n)
| 50 | 100 | 150 | 200 | 250 | 300 | 350 | 400 | 450 | 500 | 550 | 600 | 650 | 700
jki | 4.8 | 4.68 | 4.65 | 4.8 | 6.84 | 15.03 | 22.78 | 29.39 | 40.39 | 57.06 | 60.54 | 63.33 | 65.61 | 67.49
kji | 4.83 | 4.72 | 4.64 | 4.69 | 6.83 | 15.1 | 22.68 | 29.18 | 40.26 | 57.02 | 60.53 | 63.34 | 65.62 | 67.53
ijk | 3.75 | 4.08 | 4.33 | 4.45 | 4.45 | 4.45 | 4.45 | 4.47 | 7.73 | 18.77 | 20.36 | 21.67 | 22.76 | 23.71
jik | 3.93 | 4.14 | 4.36 | 4.47 | 4.52 | 4.56 | 4.57 | 4.6 | 7.96 | 19.05 | 20.59 | 21.86 | 22.92 | 23.82
kij | 1.86 | 1.78 | 2.14 | 2.3 | 2.23 | 2.18 | 2.14 | 2.12 | 2.12 | 2.13 | 2.13 | 2.14 | 2.16 | 2.22
ikj | 1.78 | 1.8 | 2.12 | 2.03 | 1.96 | 1.92 | 1.89 | 1.86 | 1.86 | 1.88 | 1.89 | 1.9 | 1.91 | 1.95
ijk / jik (1.25)
jki / kji (2.0)
kij / ikj (0.5)
Cycles per inner loop iteration

## Slide 88: Today
Cache organization and operation
Performance impact of caches
  The memory mountain
  Rearranging loops to improve spatial locality
  Using blocking to improve temporal locality

## Slide 89: Example: Matrix Multiplication
a
b
i
j
*
c
=
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i++)
for (j = 0; j < n; j++)
for (k = 0; k < n; k++)
c[i*n + j] += a[i*n + k] * b[k*n + j];
}

## Slide 90: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
First iteration:
  n/8 + n = 9n/8 misses
  Afterwards in cache: (schematic)
*
=
n
*
=
8 wide

## Slide 91: Cache Miss Analysis
Assume:
  Matrix elements are doubles
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
Second iteration:
  Again: n/8 + n = 9n/8 misses
Total misses:
  9n/8 * n2 = (9/8) * n3
n
*
=
8 wide

## Slide 92: Blocked Matrix Multiplication
c = (double *) calloc(sizeof(double), n*n);
/* Multiply n x n matrices a and b */
void mmm(double *a, double *b, double *c, int n) {
int i, j, k;
for (i = 0; i < n; i+=B)
for (j = 0; j < n; j+=B)
for (k = 0; k < n; k+=B)
/* B x B mini matrix multiplications */
for (i1 = i; i1 < i+B; i++)
for (j1 = j; j1 < j+B; j++)
for (k1 = k; k1 < k+B; k++)
c[i1*n+j1] += a[i1*n + k1]*b[k1*n + j1];
}
a
b
i1
j1
*
c
=
c
+
Block size B x B
matmult/bmm.c

## Slide 93: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
First (block) iteration:
  B2/8 misses for each block
  2n/B * B2/8 = nB/4 (omitting matrix c)
  Afterwards in cache (schematic)
*
=
*
=
Block size B x B
n/B blocks
Notes: 1/8 misses * B^2个数（每个block）
每个矩阵n/B个block
每个block只会进入Cache一次

## Slide 94: Cache Miss Analysis
Assume:
  Cache block = 8 doubles
  Cache size C << n (much smaller than n)
  Three blocks fit into cache: 3B2 < C
Second (block) iteration:
  Same as first iteration
  2n/B * B2/8 = nB/4
Total misses:
  nB/4 * (n/B)2 = n3/(4B)
*
=
Block size B x B
n/B blocks

## Slide 95: Blocking Summary
No blocking: (9/8) * n3
Blocking: 1/(4B) * n3
Suggest largest possible block size B, but limit 3B2 < C!
Reason for dramatic difference:
  Matrix multiplication has inherent temporal locality:
  But program has to be written properly

## Slide 96: 卷积神经网络

## Slide 98: 英伟达开源AI加速器NVDLA

## Slide 99: 缓存友好的卷积
2015年UCLA
引用2010次

## Slide 100
作答
练习题
根据参数确定每个高速缓存的高速缓存组数(S)、标记位数(t)、组索引位数(s)以及块偏移位数(b)，系统地址位宽（m），高速缓存容量（C）
高速缓存 | m | C | B | E | S | t | s | b
1 | 32 | 1024 | 4 | 1 |  |  |  | 
2 | 32 | 1024 | 8 | 4 |  |  |  | 
3 | 32 | 1024 | 32 | 32 |  |  |  | 
主观题
10分

## Slide 101: 练习题
根据参数确定每个高速缓存的高速缓存组数(S)、标记位数(t)、组索引位数(s)以及块偏移位数(b)，系统地址位宽（m），高速缓存容量（C）
参数计算(以1为例)：
  S=C/B/E=1024/4/1=256
  s=log2(S)=log2256=8
  b=log2(B) =log24=2
  t=m-(s+b)=32-(8+2)=22
高速缓存 | m | C | B | E | S | t | s | b
1 | 32 | 1024 | 4 | 1 | 256 | 22 | 8 | 2
2 | 32 | 1024 | 8 | 4 | 32 | 24 | 5 | 3
3 | 32 | 1024 | 32 | 32 | 1 | 27 | 0 | 5

## Slide 102: 练习题
假设高速缓存使用地址的高s位作组索引，内存块连续的片(chunk)会被映射到同一个高速缓存组
  A. 每个这样的连续的数组片中有多少个块？
  标记位数量t=m-(s+b)，每个连续的数组片由2t个块组成，数组前2t个连续的块都会映射到组0，接下来的2t个块会映射到组1，以此类推
  B. 代码运行在高速缓存形式为(S,E,B,m)=(512,1,32,32)系统上，任意时刻，存储在高速缓存中的数组块的最大数量是多少？
  标记位数量t=m-(s+b)=32-(log2512+log232)=18
  数组中前218个块映射到组1
  数组长度为4096，由(4096*4)/32=512个块组成，数组中所有的块都映射到组0，任何时刻，高速缓存至多保存一个数组块，即使数组能够全部容纳在cache中
int array[4096];
for (i=0; i<4096; i++)
sum+=array[i];

## Slide 103: 练习题： 理解cache工作原理
假设：
  内存是字节寻址的
  内存访问是1字节的字，不是4字节的字
  地址的宽度为13位
  Cache是2路组相联的(E=2)，块大小为4字节(B=4)，有8个组(S=8)
  标出下列内容字段：
    CO:cache块偏移，CI:cache组索引；CT:cache标记
 | 行0 |  |  |  |  |  | 行1 |  |  |  |  | 
组索引 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3
0 | 09 | 1 | 86 | 30 | 3F | 10 | 00 | 0 | —— | —— | —— | ——
1 | 45 | 1 | 60 | 4F | E0 | 23 | 38 | 1 | 00 | BC | 0B | 37
2 | EB | 0 | —— | —— | —— | —— | 0B | 0 | —— | —— | —— | ——
3 | 06 | 0 | —— | —— | —— | —— | 32 | 1 | 12 | 08 | 7B | AD
4 | C7 | 1 | 06 | 78 | 07 | C5 | 05 | 1 | 40 | 67 | C2 | 3B
5 | 71 | 1 | 0B | DE | 18 | 4B | 6E | 0 | —— | —— | —— | ——
6 | 91 | 1 | A0 | B7 | 26 | 2D | F0 | 0 | —— | —— | —— | ——
7 | 46 | 0 | —— | —— | —— | —— | DE | 1 | 12 | C0 | 88 | 37
12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
log24
log28

## Slide 104: 练习题
程序引用0x0E34处1字节的字，指出访问的cache条目和十六进制表示的返回的cache字节值，指出是否发生cache miss，如果发生cache miss，用—表示返回的cache缓存字节
  A.地址格式： 0x0E34
  B.内存引用：
0 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
参数 | 值
Cache块偏移(CO) | 0x 0
Cache组索引(CI) | 0x 5
Cache标记(CT) | 0x 71
Cache hits? | 是
返回cache字节 | 0x B
 | 行0 |  |  |  |  |  | 行1 |  |  |  |  | 
组索引 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3
0 | 09 | 1 | 86 | 30 | 3F | 10 | 00 | 0 | —— | —— | —— | ——
1 | 45 | 1 | 60 | 4F | E0 | 23 | 38 | 1 | 00 | BC | 0B | 37
2 | EB | 0 | —— | —— | —— | —— | 0B | 0 | —— | —— | —— | ——
3 | 06 | 0 | —— | —— | —— | —— | 32 | 1 | 12 | 08 | 7B | AD
4 | C7 | 1 | 06 | 78 | 07 | C5 | 05 | 1 | 40 | 67 | C2 | 3B
5 | 71 | 1 | 0B | DE | 18 | 4B | 6E | 0 | —— | —— | —— | ——
6 | 91 | 1 | A0 | B7 | 26 | 2D | F0 | 0 | —— | —— | —— | ——
7 | 46 | 0 | —— | —— | —— | —— | DE | 1 | 12 | C0 | 88 | 37

## Slide 105: 练习题
程序引用0x0DD5处1字节的字，指出访问的cache条目和十六进制表示的返回的cache字节值，指出是否发生cache miss，如果发生cache miss，用—表示返回的cache缓存字节
  A.地址格式： 0x0DD5
  B.内存引用：
0 | 1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 1
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
参数 | 值
Cache块偏移(CO) | 0x 1
Cache组索引(CI) | 0x 5
Cache标记(CT) | 0x 6E
valid? | 否
Cache hits? | 否
返回cache字节 | —
 | 行0 |  |  |  |  |  | 行1 |  |  |  |  | 
组索引 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3
0 | 09 | 1 | 86 | 30 | 3F | 10 | 00 | 0 | —— | —— | —— | ——
1 | 45 | 1 | 60 | 4F | E0 | 23 | 38 | 1 | 00 | BC | 0B | 37
2 | EB | 0 | —— | —— | —— | —— | 0B | 0 | —— | —— | —— | ——
3 | 06 | 0 | —— | —— | —— | —— | 32 | 1 | 12 | 08 | 7B | AD
4 | C7 | 1 | 06 | 78 | 07 | C5 | 05 | 1 | 40 | 67 | C2 | 3B
5 | 71 | 1 | 0B | DE | 18 | 4B | 6E | 0 | —— | —— | —— | ——
6 | 91 | 1 | A0 | B7 | 26 | 2D | F0 | 0 | —— | —— | —— | ——
7 | 46 | 0 | —— | —— | —— | —— | DE | 1 | 12 | C0 | 88 | 37

## Slide 106: 练习题
程序引用0x1FE4处1字节的字，指出访问的cache条目和十六进制表示的返回的cache字节值，指出是否发生cache miss，如果发生cache miss，用—表示返回的cache缓存字节
  A.地址格式： 0x1FE4
  B.内存引用：
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
参数 | 值
Cache块偏移(CO) | 0x 0
Cache组索引(CI) | 0x 1
Cache标记(CT) | 0x FF
Cache hits? | 否
返回cache字节 | —
 | 行0 |  |  |  |  |  | 行1 |  |  |  |  | 
组索引 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3
0 | 09 | 1 | 86 | 30 | 3F | 10 | 00 | 0 | —— | —— | —— | ——
1 | 45 | 1 | 60 | 4F | E0 | 23 | 38 | 1 | 00 | BC | 0B | 37
2 | EB | 0 | —— | —— | —— | —— | 0B | 0 | —— | —— | —— | ——
3 | 06 | 0 | —— | —— | —— | —— | 32 | 1 | 12 | 08 | 7B | AD
4 | C7 | 1 | 06 | 78 | 07 | C5 | 05 | 1 | 40 | 67 | C2 | 3B
5 | 71 | 1 | 0B | DE | 18 | 4B | 6E | 0 | —— | —— | —— | ——
6 | 91 | 1 | A0 | B7 | 26 | 2D | F0 | 0 | —— | —— | —— | ——
7 | 46 | 0 | —— | —— | —— | —— | DE | 1 | 12 | C0 | 88 | 37

## Slide 107: 练习题
列出所有的在组3中会命中的十六进制内存地址
组3包含一个有效行，标记为0x32，有效位为1，4个地址会命中，这些地址的有效形式为：
4个十六进制地址为：
  0x 064C, 0x 064D, 0x 064E, 0x 064F
 | 行0 |  |  |  |  |  | 行1 |  |  |  |  | 
组索引 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3 | 标记位 | 有效位 | 字节0 | 字节1 | 字节2 | 字节3
3 | 06 | 0 | —— | —— | —— | —— | 32 | 1 | 12 | 08 | 7B | AD
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 |  | 
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 0 | 0
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO
0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 1 | 1 | 1
CT | CT | CT | CT | CT | CT | CT | CT | CI | CI | CI | CO | CO

## Slide 108: 练习题： 转置矩阵
假设：
  Sizeof(int)=4
  Src数组从地址0开始，dst数组从地址16开始
  只有一个L1 cache，直接映射、直写和写分配，块大小为8字节
  Cache大小为16字节，开始为空
  Src和dst数组访问分别是读和写不命中的唯一来源
Typedef int array[2][2]
Void transpose1(array dst, array src)
{
int I,j;
for(i=0;i<2;i++){
for(j=0;j<2;j++){
dst[j][i]=src[i][j];
}
}
}
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
cache
Main
memory
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
m
m
i=0
j=0

## Slide 109: 练习题：转置矩阵
假设：
  Sizeof(int)=4
  Src数组从地址0开始，dst数组从地址16开始
  只有一个L1 cache，直接映射、直写和写分配，块大小为8字节
  Cache大小为16字节，开始为空
  Src和dst数组访问分别是读和写不命中的唯一来源
Typedef int array[2][2]
Void transpose1(array dst, array src)
{
int I,j;
for(i=0;i<2;i++){
for(j=0;j<2;j++){
dst[j][i]=src[i][j];
}
}
}
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
cache
Main
memory
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
m
m
m
m
i=0
j=1

## Slide 110: 练习题： 转置矩阵
假设：
  Sizeof(int)=4
  Src数组从地址0开始，dst数组从地址16开始
  只有一个L1 cache，直接映射、直写和写分配，块大小为8字节
  Cache大小为16字节，开始为空
  Src和dst数组访问分别是读和写不命中的唯一来源
Typedef int array[2][2]
Void transpose1(array dst, array src)
{
int I,j;
for(i=0;i<2;i++){
for(j=0;j<2;j++){
dst[j][i]=src[i][j];
}
}
}
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
cache
Main
memory
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
m
m
m
m
m
m
i=1
j=0

## Slide 111: 练习题： 转置矩阵
假设：
  Sizeof(int)=4
  Src数组从地址0开始，dst数组从地址16开始
  只有一个L1 cache，直接映射、直写和写分配，块大小为8字节
  Cache大小为16字节，开始为空
  Src和dst数组访问分别是读和写不命中的唯一来源
Typedef int array[2][2]
Void transpose1(array dst, array src)
{
int I,j;
for(i=0;i<2;i++){
for(j=0;j<2;j++){
dst[j][i]=src[i][j];
}
}
}
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
cache
Main
memory
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
m
m
m
h
m
m
m
m
i=1
j=1

## Slide 112: 练习题：转置矩阵
假设：
  Sizeof(int)=4
  Src数组从地址0开始，dst数组从地址16开始
  只有一个L1 cache，直接映射、直写和写分配，块大小为8字节
  Cache大小为32字节，开始为空
  Src和dst数组访问分别是读和写不命中的唯一来源
Typedef int array[2][2]
Void transpose1(array dst, array src)
{
int I,j;
for(i=0;i<2;i++){
for(j=0;j<2;j++){
dst[j][i]=src[i][j];
}
}
}
a[0][0]
a[0][1]
a[1][0]
a[1][1]
cache
Main
memory
a[0][0]
a[0][1]
a[1][0]
a[1][1]
b[0][0]
b[0][1]
b[1][0]
b[1][1]
m
h
m
h
m
h
m
h
b[0][0]
b[0][1]
b[1][0]
b[1][1]

## Slide 113
Cache命中率与容量的关系
容量(k字节）
100℅
命中率
40℅
60℅
95℅
1K
8K
32K
256K
512K
128K
90℅
80℅

## Slide 114
Cache命中率与块大小的关系
Notes: Increasing the block size usually decreases the miss rate.
A more serious problem is that the miss penalty goes up since it is primarily determined by the time to fetch the block from the next lower level of the hierarchy and load it into the cache.

## Slide 115: 直接映象Cache命中率与块大小分析
考虑如下的访问序列
0 1 2 3 4 3 4 15
0
1
2
3
4
3
4
15
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(0)
00 Mem(0)
00 Mem(1)
00 Mem(2)
miss
miss
miss
miss
miss
miss
hit
hit
00 Mem(0)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01 Mem(4)
00 Mem(1)
00 Mem(2)
00 Mem(3)
01
4
11
15
00 Mem(1)
00 Mem(2)
00 Mem(3)
  8 次请求, 6次失效 (命中率 = 0.25,失效率 = 0.75)
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Reference string is word addresses (or block number since we are using one word blocks) – i.e., the low order two bits used to selected the byte in the 32-bit word are ignored

## Slide 116: 直接映象Cache命中率与块大小分析
让每个cache块多于1个字节
0 1 2 3 4 3 4 15
0
1
2
3
4
3
4
15
00 Mem(1) Mem(0)
miss
00 Mem(1) Mem(0)
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
hit
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
miss
00 Mem(3) Mem(2)
00 Mem(1) Mem(0)
01
5
4
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
hit
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
00 Mem(3) Mem(2)
01 Mem(5) Mem(4)
miss
11
15
14
  8 次请求, 4次失效 (命中率= 0.5, 失效率= 0.5)
0000 0001 0010 0011 0100 0011 0100 1111
Notes: For lecture
Show the 4-bit address mapping – 2-bits of tag, 1-bit of set address (index), 1-bit of word-in-block select

## Slide 117: 替换策略
（1）随机数替换算法
  当需要找替换块时，产生一个随机数，它就是被替换的块号。
  这种算法完全不反映程序的局部性特点，只是算法简单、实现容易。
  结论：不是一个好的算法。
（2）FIFO算法（先进先出）
  总是把一组中最先调入 Cache存储器的字块替换出去，它不需要随时记录各个字块的使用情况，所以实现容易，开销小。
  缺点：它没有根据访存局部性原理，最早调入的块可能是以后还要用到的，或者是经常用到的。
（3）LRU算法（近期最少使用法）
  把Cache中近期最少使用的块替换出去。

## Slide 118
作答
练习题 紧密循环cache命中率计算
硬件假设：
  块大小：16字节
  Sizeof(int)=4
  Cache大小1024字节
计算：
  读总数
  Cache不命中的读总数
  不命中率
Struct algae_position{
int x,y;
}
Struct algae_position grid[16][16];
Int total_x=0, total_y=0;
Int I,j;
For(i=0;i<16;i++){
for(j=0;j<16;j++){
total_x+=grid[i][j].x;
}
}
For(i=0;i<16;i++){
for(j=0;j<16;j++){
total_y+=grid[i][j].y;
}
}
主观题
10分

## Slide 119: 练习题： 紧密循环cache命中率计算
硬件假设：
  块大小：16字节
  Sizeof(int)=4
  Cache大小1024字节
计算：
  读总数
  Cache不命中的读总数
  不命中率
Struct algae_position{
int x,y;
}
Struct algae_position grid[16][16];
Int total_x=0, total_y=0;
Int I,j;
For(i=0;i<16;i++){
for(j=0;j<16;j++){
total_x+=grid[i][j].x;
}
}
For(i=0;i<16;i++){
for(j=0;j<16;j++){
total_y+=grid[i][j].y;
}
}
读总数为：512
缓存不命中的读总数：256
不命中率：256/512=50%

## Slide 120: 练习题
读总数为：512
缓存不命中的读总数：
  每次j循环前1024字节产生8个不命中
  后1024字节与前一半循环映射冲突，产生8个不命中
  16次循环共16*16=256次不命中
不命中率：256/512=50%
grid[0][0].y
grid[0][0].x
grid[0][1].y
grid[0][1].x
Cache block(B=16)
Cache block(B=16)
B[0]
B[63]
1024字节
grid[7][14].y
grid[7][14].x
grid[7][15].y
grid[7][15].x
……
……
grid[8][0].y
grid[8][0].x
grid[8][1].y
grid[8][1].x
grid[15][14].y
grid[15][14].x
grid[15][15].y
grid[15][15].x
……
For(i=0;i<16;i++){
for(j=0;j<16;j++){
total_x+=grid[j][i].x;
total_y+=grid[j][i].y;
}
}

## Slide 121: 练习题
读总数为：512
缓存不命中的读总数：
  顺序步长为1访问，不命中为强制不命中
  不命中数为64*2=128
不命中率：128/512=25%
缓存加倍，与数据相同时，强制不命中数量不会改变
grid[0][0].y
grid[0][0].x
grid[0][1].y
grid[0][1].x
Cache block(B=16)
Cache block(B=16)
B[0]
B[63]
1024字节
grid[7][14].y
grid[7][14].x
grid[7][15].y
grid[7][15].x
……
……
grid[8][0].y
grid[8][0].x
grid[8][1].y
grid[8][1].x
grid[15][14].y
grid[15][14].x
grid[15][15].y
grid[15][15].x
……
For(i=0;i<16;i++){
for(j=0;j<16;j++){
total_x+=grid[i][j].x;
total_y+=grid[i][j].y;
}
}

## Slide 122: Cache Summary
Cache memories can have significant performance impact
You can write your programs to exploit this!
  Focus on the inner loops, where bulk of computations and memory accesses occur.
  Try to maximize spatial locality by reading data objects with sequentially with stride 1.
  Try to maximize temporal locality by using a data object as often as possible once it’s read from memory.